## Slide 1: Vision Transformer Approach to Superresolution Single-Molecule Localization Imaging
Muzna Yumman and Yi Sun
Electrical Engineering Department, The City College of New York
Research Background
Single-molecule localization microscopy (SMLM) is a family of super-resolution fluorescence imaging techniques that overcome the Abbe diffraction limit by localizing individual fluorescent emitters across thousands of frames [3,4,5,6].
Deep learning has become central to SMLM, enabling faster and more accurate localization than classical fitting methods. Vision Transformers (ViTs) extend this by modeling global spatial relationships using self-attention [1,2].
Objectives
Develop a ViT for sub-pixel localization of 1–5 emitters in 7×7 pixels SMLM data frames with 10 nm resolution.
Achieve 10 nm precision by treating localization as classification on a 70×70 subpixel grid (4,900 classes), predicting M emitter locations per frame through a multi-head architecture.
METHODS
Data Generation
Data frames are synthesized using a 2D Gaussian PSF model (NA = 1.4, λ = 723 nm, 100 nm/pixel) with Poisson photon noise and EMCCD readout noise. Each 7×7 frame contains M = 1–5 randomly positioned emitters with ground-truth coordinates at 10 nm sub-pixel resolution.
Network Architecture
The ViT uses patch size = 1, treating each pixel as a token (49 tokens per frame). Tokens are projected to 64 dimensions via 1×1 convolution with learnable positional embeddings.
Four Transformer encoder blocks (4-head self-attention, MLP 64→128→64, GELU, residual connections) process the sequence.
Global max pooling produces a single 64-dim vector, fed to an MLP head outputting M × 4,900 logits over a 70×70 sub-pixel grid (10 nm resolution).
Training Procedure
Separate models are trained for M = 1–5 using Adam (lr = 3×10⁻⁴), batch size 64, for 20 epochs.
Loss: sum of cross-entropy across M heads, with emitters sorted by class index for stable assignment.
Evaluation and Benchmarking
Localization accuracy is measured by RMSMD (root mean square minimum distance), a symmetric nearest-neighbor metric reported in nanometers.
NETWORK ARCHITECTURE
Results – 1
Results – 2
Conclusions
ViT achieves localization accuracy close to EM and significantly outperforms UGIA-F, confirming that a data-driven approach can approach model-based performance without knowledge of the imaging system parameters.
Future work will extend the framework to SMLM data movies, variable emitter counts, larger frames, and experimental datasets.
References
[1] Vaswani, A., et al. Advances in Neural Information Processing Systems 30 (NeurIPS), 5998–6008 (2017).
[2] Dosovitskiy, A., et al. International Conference on Learning Representations (ICLR) (2021).
[3] Sun, Y. Optics Express 32(19), 33779–33794 (2024).
[4] Sun, Y. Scientific Reports 8(1), 17211 (2018).
[5] Sun, Y. Journal of Biomedical Optics 18(11), 111418 (2013). [6] Sun, Y., et al. Quantitative BioImaging Conference (QBI) (2014).
Results – 3
Comparison of Ground Truth, UGIA-F, EM, and ViT reconstructions for multi-emitter
data frames (M=1 to 5)
.
Acknowledgments
  This work is partly supported by National Science Foundation (CCF-2313072) and Army Research Office (W911NF-23-1-0189).
Learning curves for the ViT (M=5). Left: Training and validation loss converge within 20 epochs. Right: RMSMD (nm) decreases steadily with training.
Average RMSMD vs. Number of emitters: EM < ViT ≪ UGIA-F, confirming ViT achieves near-EM accuracy.
Proposed ViT architecture: 7×7 SMLM frames are tokenized at patch size 1 (49 tokens), encoded via four Transformer blocks, and mapped to M×4,900 sub-pixel class logits for 10 nm localization.